‘Default’ Settings
Device name: linvor
Device PIN: 1234
115200 Baud
8 Data Bits
1 Stop Bit
No Parity

‘Default’ UART Settings for AT Command Mode
To use AT Command mode, pull pin 34 of the Bluetooth module high at power on. PILED boards come with the Bluetooth module pre-programmed for the above default settings. It is easy to change various Bluetooth settings, such as the device name, PIN, and baud rate. If you manage to accidentally change the baud rate to something you can’t communicate with, the AT Command mode will still operate at the below settings, and you can change it back.
38400 Baud
8 Data Bits
1 Stop Bit
No Parity

Protocol Format
Issue AT commands to the UART (not over Bluetooth…). You can do this easily by reprogramming the PILED with the code that simply sends commands to the UART as explained below. The pad marked ‘AT’ must be connected for the 3.3V rail for the module to accept AT commands. Once you are done programming the Bluetooth module, disconnect the ‘AT’ pin and re-power up the board – this will set the Bluetooth module back to communication mode. The Linvor AT commands are terminated by a timeout. The timeout is short enough that AT commands cannot be entered by hand. If using a terminal, paste in the commands. Do not terminate them with CR/LF.
AT Commands
‘Ping’ Test
The ‘ping’ test simply responds with “OK” letting you know communication was successful.
Send: AT
Response: OK

Example:
AT
Ok
Set Baud Rate
Sets the HC07 UART baud rate. Baud rate is set by an hexadecimal index from '1' to 'C'.
Indices are:
1: 1200
2: 2400,
3: 4800,
4: 9600,
5: 19200,
6: 38400,
7: 57600,
8: 115200,
9: 230400,
A: 460800,
B: 921600,
C: 1382400
Send: AT+BAUD<index>
Response: OK<baud rate>

Example:
AT+BAUD8
OK115200
Set Bluetooth Device Name
Sets Bluetooth Device Name
Send: AT+NAME<device name>
Response: OK<device name>

Example:
AT+NAMEPILED
OKPILED
Set Bluetooth PIN Code
Sets the security code needed to connect to the device.
Send: AT+PIN<4 digit code>
Response: OK<4 digit code>

Example:
AT+PIN1337
OK1337
Check Firmware Revision
Get The Firmware Revision Number. This document reflects the commands for 'Linvor1.5'.
Send: AT+VERSION
Response: Linvor1.5

Example:
AT+VERSION
Linvor1.5